## Slide 1
AAVISHKAR
Research Convention
Title of the research project
Integrated Railway Maintenance Prioritization and Constraint-Based Block Planning for Asset Availability
Category
5 — Engineering and Technology
Level
________________
Slot / Code No.
________________
Notes: Open with the title only. Say that the level and the slot or code number will be the ones issued at registration, and that you will introduce yourself by that number. Do not say your name, college, department, or team. Give the title once, slowly: integrated railway maintenance prioritisation and constraint-based block planning for asset availability. Then move on. About 20 seconds.

## Slide 2
PROBLEM AND OBJECTIVE
Maintenance is still requested department by department
What is fragmented
Engineering, traction, and signalling keep defect records in TMS, SMMS, and TDMS. Each department asks for its own block through BDMS. COA holds corridor availability. The timetable is a separate document. [1]
Why the gap matters
Mail/Express punctuality on Indian Railways was 73.62% in 2023–24 and 77.12% in 2024–25. Asset maintenance is one stated cause of delay. [2] In a 2017 audit of selected heavy-traffic sections, non-availability of blocks was the stated reason deep screening fell overdue. [4]
Research objective
Can separate maintenance records and a working timetable be turned into one explainable priority, a separate escalation forecast, shared possessions, and a feasible block a person still has to approve?
Rolling Block, notified on 30 November 2023, already asks for integrated maintenance to be planned ahead. This prototype tests one way to do that on a modelled corridor. [3]
Prototype evidence. Not a live railway deployment.
2 / 6
Notes: The problem is coordination, not a claim that the railway has no maintenance process. Track, traction, and signalling each keep their own defect lists — TMS, SMMS, and TDMS — and each asks for a block through BDMS. The control office application holds the corridor, and the working timetable is another document. Smart India Hackathon problem statement 26027, from the Ministry of Railways, describes that split as a cause of poor block use.
Put the punctuality figures in their population and years. For Mail and Express trains on Indian Railways, Lok Sabha Unstarred Question 3976, answered on 12 August 2026, gives 73.62 percent in 2023–24 and 77.12 percent in 2024–25. The same reply gives 77.43 percent for 2025–26. Asset maintenance is one of the causes the Ministry lists, alongside fog, path constraints, alarm-chain pulling, and other events. Do not say punctuality is falling. It moved up between those two full years.
The older audit is historical. CAG Report 45 of 2017, tabled in March 2018, looked at selected heavy-traffic sections. At the exit conference in August 2017, Railway Board said non-availability of blocks was the main reason deep screening in those observations was overdue. That is not a figure for today’s network.
The research question is whether one prototype can keep three judgements separate: an explainable urgency score, a separate forecast of days to a critical severity, and a block window that a person still approves. Mention Rolling Block, notified on 30 November 2023, as the operating idea this work lines up with: integrated maintenance planned ahead, not invented on the day. About 70 seconds.

## Slide 3
METHOD
One pipeline. The numbers are not merged.
TMS, SMMS, TDMS, COA, and WTT are the intended feeds. In this build they are file readers plus an encoded CSMT–Pune model, not live railway servers.
TMS Track
SMMS Signalling
TDMS Traction
COA Corridor
WTT Timetable
1
Read and check
Parse each export. A bad row is rejected with a reason.
2
AI-1 review
Local rules propose findings. A quote must be on the page. A person applies ready rows.
3
Formula 1
Explainable urgency from severity, overdue days, TSR, and traffic.
4
Days to critical
A separate forecast. It does not replace Formula 1.
5
Formula 2
Same line and feeder, next job within 3 km, one possession.
6
CP-SAT
OR-Tools searches a legal window under Rules A, B, and C.
7
Dashboard
Three policies are shown. A person sanctions, shifts, or rejects.
Prototype evidence. Not a live railway deployment.
3 / 6
Notes: Walk the diagram from the top. The five names are the feeds the problem statement asks for. In this build they are readers for export files and a locally encoded CSMT to Pune corridor of 192 kilometres. Say clearly that production endpoints are not connected.
Then the seven steps. Reading and checking rejects a bad row without dropping the whole file. AI-1 is the report reader. On an ordinary upload it uses local sentence rules. It proposes a finding only when the wording matches a known defect phrase, and a second check keeps the finding only when the quoted words are actually on the page. A person applies the complete rows. It is not a trained generative model, and it does not score urgency.
Formula 1 then scores the open job. Beside it, a gradient-boosting model estimates days until severity reaches 80. Those two numbers stay separate. Formula 2 groups jobs on the same running line and the same power feeder when the next defect is within 3 kilometres. Google OR-Tools CP-SAT searches for a window that satisfies the hard rules. The dashboard shows the result for a person to sanction. About 80 seconds.

## Slide 4
CONTRIBUTION
The combination is the research claim
Shared records
Department exports are normalised into one defect shape. Source severity is kept as reported. It is not rewritten as the urgency score.
Explainable priority
Formula 1 is written down: safety, overdue days, an active speed restriction, and how busy the line is. The screen shows 0–100. The solver can use the unclipped score.
A separate forecast
Gradient boosting estimates days until severity reaches 80. Training labels are synthetic. The forecast is shown beside Formula 1, not inside it.
One possession
Formula 2 packs compatible jobs on the same line and feeder within 3 km. Work time becomes the longest job plus 15 minutes, instead of a fresh visit for each job.
A feasible window
CP-SAT must keep trains and the gang apart, protect Premium and Superfast trains from induced delay, cap other delay, and respect the machine pool and power isolation.
A human decision
Punctuality-First, Asset-First, and Mega-Block reweight the same constraints. AI-1 only prepares evidence-linked rows. It does not choose the block.
Prototype evidence. Not a live railway deployment.
4 / 6
Notes: This slide is the contribution, so do not read every box. Say that a scheduling screen by itself is not the claim. The claim is that the steps stay inspectable and still fit together.
Formula 1 is written down. Safety comes from severity, then overdue days, then whether a temporary speed restriction is already on, then a traffic index for that line. The console shows a score from 0 to 100. The solver can keep the unclipped score so two severe jobs do not look identical.
The machine-learning piece does not replace that score. It forecasts days to criticality. Say, if asked, that the labels are synthetic. Do not quote R-squared as field accuracy; that belongs with the limits.
Formula 2 is how repeated mobilisation is reduced: one possession instead of one visit per job. CP-SAT is how the possession is allowed onto the timetable. Rule A keeps a train and a gang out of the same place at the same time. Rule B gives Premium and Superfast trains no induced delay. Rule C caps delay for other types. The machine pool in the model is one ballast cleaner, two tie tampers, and two tower wagons. A power block also requires isolation.
The three policies — Punctuality-First, Asset-First, and Mega-Block — change the weights. They do not hide a single answer. AI-1’s job ends when a reviewed record enters the backlog. About 70 seconds.

## Slide 5
PROTOTYPE EVALUATION
What was tested, and what it showed
Encoded CSMT–Pune corridor model: 192 km.
24-hour working timetable: 170 modelled services.
Encoded demonstration backlog: 14 defects, 11 bundles.
One 7-day run from 24 September 2026 placed 10 of those 14 defects. Four stayed for a later day. An unsafe window was not forced.
Three multi-defect clusters: 450 job-minutes if done separately, 330 when bundled. Saved: 120 minutes (26.7%).
Bundled work minutes on the encoded backlog
Chart: Job minutes
| S1 DN Fast | S2 DN | S3 Mid
Separate jobs | 150 | 180 | 120
One bundle | 105 | 135 | 90
These are prototype simulations on local demo data. They are not divisional operating results. The live console backlog starts empty until a reviewed report is applied.
Prototype evidence. Not a live railway deployment.
5 / 6
Notes: Say the test conditions before the percentages. The corridor is a 192 kilometre encoded model from CSMT to Pune Junction. The timetable is a 24-hour model of 170 services, not a live control-office feed. The backlog is 14 encoded demonstration defects, grouped into 11 bundles. The console’s live list actually starts empty until someone applies a reviewed report. These 14 defects are the demonstration catalog used for the test.
The chart is Formula 2 on the three clusters that contain more than one defect. If each job kept its own duration, the minutes are 150, 180, and 120. Bundled, using the longest job plus 15 minutes, they are 105, 135, and 90. Together that is 450 minutes against 330, so 120 minutes, or 26.7 percent, of those job minutes. These are maintenance-work minutes in the model. They are not measured minutes of train delay on the ground.
The week result is one simulation, from 24 September 2026 through seven days. Ten of the 14 defects were placed in a feasible window. Four were left for later. Where a night window could not hold a job, the solver reported infeasible and the plan moved or split the work rather than forcing the train conflict. Do not call this a field week. About 80 seconds.

## Slide 6
CONCLUSION
What this demonstrates, and what it does not
Contribution
The prototype shows a full path from separate maintenance records to a conflict-checked block: validate, review evidence, score urgency, forecast escalation separately, bundle nearby work, then let CP-SAT search a legal window for a person to sanction.
Limits and next evidence
Inputs are local and simulated. AI-1’s ordinary reader is rule-based and misses unfamiliar wording. The forecast is trained on synthetic labels, not real defect histories. A field claim needs authorised feeds and a shadow-mode trial.
[1] Ministry of Railways, SIH 2026 problem statement SIH26027.
[2] Lok Sabha Unstarred Question 3976, answered 12 August 2026. Mail/Express punctuality on Indian Railways.
[3] Rajya Sabha Starred Question 62, answered 5 December 2025. Rolling Block, Gazette notification 30 November 2023.
[4] CAG Report No. 45 of 2017, tabled 13 March 2018. Selected heavy-traffic sections. Historical.
Prototype evidence. Not a live railway deployment.
6 / 6
Notes: Close on four sentences. The prototype demonstrates a path from separate records to a block a person can defend. The contribution is the split between evidence-backed reading, explainable urgency, a separate forecast, spatial bundling, and constraint solving. The important limits are local demo inputs, a rule-based report reader, and a forecast that has not seen real defect histories. The next evidence is authorised access, a shadow-mode comparison against today’s block decisions, and a held-out set of real reports.
If there is time, point at the four references and stop. Do not add a name or a team. Leave the last seconds for the judges. About 60 seconds. The whole talk should finish inside seven minutes, with the warning bell in mind at six.